## Slide 1: Forecasting Wind Power
Advanced Time series Analysis - Exam
Group:
Jacob Hægh
Marcos Bauch Mira
Asher Kite
Abbie Langhave

## Slide 2: Table of Contents
1. Project Overview
2. Data Description and Handling
3. Modelling Approach
4. Linear Models
  Persistence and AR(p) models
5. Nonlinear Models
  Sigmoid of Wind Speed, Sine/Cosine of Wind Direction, etc.
6. Model Evaluation
  AIC and BIC, RMSE
7. Conclusion
8. Future Work Suggestions
  SDE Modelling with ctsmTMB, Adaptive GARCH Modelling,

## Slide 3: Motivation
Renewable energy is expanding rapidly, with wind power playing a growing role
Wind variability poses challenges for grid stability and energy markets
Problem
Accurate short-term forecasts of wind power are essential
Wind fluctuations complicate operations for power plants and market planning
Project Aim
Develop a model that uses weather data to predict hourly wind power output
Project Overview

## Slide 4: Data Description
Dataset: Hourly observations from a wind farm in Klim, NW Jutland.
Variables: Measured power, 1-,2-and 3-hr forecasted wind speed, wind direction and temperature, timestamps and time-of-year indicator
Power Time Series:
Shows hourly wind power over the observation period
Highlights variability and periods of low/high generation
Power vs. Wind Speed:
Strong nonlinear relationship between wind speed and power
Power rises with wind speed up to the turbine’s rated capacity

## Slide 5: Data Handling
Largest gaps occur in weather forecasts
Power data has smaller missing segments
Three strategies for handling missing values:
  X_p: Fill using persistence
  X_c: Clip large gaps, fill remaining missing values
  X_d: Drop all rows with any missing values

## Slide 6: Modelling Approach
Adaptive forecasting using Recursive Least Squares (RLS)
Models updated sequentially as new data becomes available
Forecast horizons: 1-, 2-, and 3-hour ahead wind power
Model complexity increased step by step to improve accuracy

## Slide 7: Recursive Least Squares (RLS)
Sequential method for estimating model parameters over time
Updates coefficients at each time step using new observations
Uses a forgetting factor to emphasize recent data
Well suited for non-stationary time series such as wind power

## Slide 8: Training and Evaluation Setup
First 50% of the data used to initialize model parameters
Remaining 50% used for testing and evaluation
Burn-in period of 100 time steps excluded from performance metrics
Forecast accuracy evaluated using RMSE

## Slide 9: Model Overview
Multiple models tested with increasing complexity
Baseline: Persistence model
Linear models: AR(1) and AR(4)
Nonlinear models: Wind speed, time, direction, and temperature effects
All models estimated using Recursive Least Squares

## Slide 10: Persistence Model
Forecast equals the most recent observed power value
AR(1) Model
Linear dependence on the most recent power observation
AR(4) Model
Uses multiple past power values to capture temporal structure
Baseline and Linear Models
AR models estimated using Recursive Least Squares

## Slide 11: Nonlinear Wind Speed-Power Relationship
Wind power has a nonlinear dependence on wind speed
Linear models cannot capture this behavior effectively
Introduced a sigmoid function to model the power curve

## Slide 12: Extended Nonlinear Models
Added time-of-year effects using sine and cosine terms
Included wind direction through circular (sin/cos) features
Improved sigmoid parameters using training data
Applied physical bounds to predicted power values
Final model also incorporates temperature forecasts

## Slide 13: Model Evaluation

## Slide 14: Model Summary

## Slide 15: Forecast Accuracy (RMSE)
Models compared using RMSE for 1-, 2-, and 3-hour ahead forecasts
Forecast accuracy generally improves with increased model complexity
Performance gains differ across forecast horizons

## Slide 16: Conclusion
Adaptive models improve short-term wind power forecasting
Capturing the nonlinear wind speed–power relationship is critical
Additional nonlinearities provide smaller, horizon-dependent gains
The best-performing model differs slightly by forecast horizon

## Slide 17: Thank you!

## Slide 18: Future Work – Suggestions
Formulating SDE using the CSTM library
Formulating a GARCH model

## Slide 19: References
[1] https://en.wikipedia.org/wiki/Recursive_least_squares_filter

## Slide 20: d
Adaptive forecasting using Recursive Least Squares (RLS)
Models updated sequentially as new data becomes available
Forecast horizons: 1-, 2-, and 3-hour ahead wind power
Model complexity increased step by step to improve accuracy